## Slide 1: Singing Synthesizer
Michael Nye
11-752 Spring 2014
Final Project

## Slide 2: GOALS
To create a singing synthesizer featuring…
  MIDI control for performance
  English-like voicing of vowels and consonants
  Neutral tone
  Expressive control of volume, vibrato, etc.

## Slide 3: OPERATION
Note attacks with a consonant
  Supports H, F, V, S, Z, T, D, P, B, K, G, L, M, N
Note holds on a consonant
  Supports A, E, I, O, U
Held and attack sounds are changed by MIDI keys
Glides between pitches without rearticulating
Variable Volume, vibrato, tremolo, attack/release time
  Adjustable with MIDI sliders

## Slide 4: CONTROLS
Sung notes (C2-E3)
A
E
I
O
U
H
T
D
F
V
L
M
N
G
K
B
P
S
Z
Volume
Vibrato
Tremolo
Attack
Release
Glide
Interpolate

## Slide 5: DATA COLLECTION
Source: me!
Recorded ascending chromatic scales
  Each note held for 2-3 seconds
  Each note is separated by silence
  One recording for each sound
Saved as wav files for training

## Slide 6: MODEL SELECTION
Linear Predictive Coding
  Trains a filter with the same resonances as its source
  Good for simulating formants
Lattice Filter Representation
  Different form of the same filter
  Lattice coefficients are less sensitive to numerical errors, and allow for interpolation between sounds

## Slide 7: MODEL SELECTION
Lattice Coefficient Interpolation from A to I

## Slide 8: TRAINING PROCEDURE
Training is done in MATLAB
For each sound…
  Read in a recorded wave file
  Segment the recording to remove silence
  Train a single LPC model for the entire scale
  Normalize the gains between each filter
  Export a data file with the coefficients

## Slide 9: SYNTHESIZER IMPLEMENTATION
Implemented in C++ using MIDI
Generates a pulse train and white noise
  Pulse train is used for voicing
  White noise is used for consonants
    Lots of hand-tuning was used for mixing durations for different consonants

## Slide 10: EVALUATION
Individual sounds were built one at a time
Primary evaluation was my own subjective appraisals while listening to performed notes
Secondary evaluation was performed by my roommate and a friend
  Only when I felt I had made substantial progress

## Slide 11: FINAL PERFORMANCE
Playability is very high
  But live parameter adjustment requires practice
  Could be programmed
Vowel sounds are great
Some consonants are great, while others are hard to distinguish

## Slide 12: DEMO

## Slide 13: QUESTIONS?